## Slide 1: When can we trust AI-generated tests ? Uncertainty quantification for risk-based testing of autonomous CPS
PhD RESEARCH PROPOSAL
Za Vinh Le
Notes: Good morning. Thank you for the invitation. In the next 20 minutes I will argue that LLM-generated tests need a trust signal, show a working prototype that quantifies their uncertainty for an autonomous-driving function, and propose how I would turn its gaps into the four InnoGuard objectives over three years.

## Slide 2: LLMs now write tests for safety-relevant systems — confidently
Foundation models enter CPS engineering: scenario realism checks, oracles, digital twins, robot testing [8, 10, 11, 7]
LLM test generation is now mainstream in software testing research [27]
But a well-formed test can still be wrong: it may miss the requirement, carry a wrong oracle, or catch no fault
In ACPS a wrong test is a safety risk: false confidence in an emergency-braking or cut-in function
In my experiment (gpt-5.6-luna, 70 tests)
97%
average self-reported confidence
87%
of its tests are actually correct (fault-injection ground truth)
Notes: Prof. Ali's group and colleagues already use foundation models across CPS engineering. LLM-based test generation is mainstream. The open problem is trust: a syntactically valid test can be irrelevant, can have a wrong oracle, or can be useless at finding faults. My own data shows the model says it is 97% sure while only 87% of its tests are correct — so self-reported confidence is not a usable trust signal.

## Slide 3: The position's four objectives, as research questions
O1
New UQ metrics
Which signals reveal that an AI-generated test artefact is untrustworthy — for black-box and white-box models?
O2
Risk & trustworthiness
How should quantified uncertainty drive accept / review / reject decisions under safety risk?
O3
Uncertainty vs. quality
How does uncertainty relate to correctness, fault-detection power and cost of the generated tests?
O4
Future AI models
Do the metrics transfer to newer large models and to quantum machine learning models?
InnoGuard: Hybrid and Generative Intelligence for Trustworthy Autonomous CPS, MSCA Doctoral Network, 2024–2028 [30]
Notes: This is how I read the four objectives of the position, phrased as questions. Everything that follows — the prototype, its gaps and the plan — is organised around O1 to O4.

## Slide 4: Building on uncertainty-wise CPS testing
Uncertainty in CPS & DL
U-Taxonomy & uncertainty-wise test modelling and generation [3, 2, 1]
Uncertainty-aware prediction validator for DL in CPS [4]
Uncertainty-wise multi-level oracles; elevator robustness under uncertainty [6, 5]
Uncertainty & quality of VLA-enabled robots [7]
ADS testing & falsification
Avoidable-collision scenario generation [12]
Parameter coverage for ADS testing under uncertainty [13]
Robustness-guided falsification of AI-enabled hybrid systems [15, 14]
LLMs assessing driving-scenario realism [8]
Oracles & industrial CPS
ML-based test oracles for elevator dispatching [16]
Generated metamorphic relations for CPS [17]
Seeding strategies for search-based test selection [18]
Foundation models for CPS engineering: road ahead [10, 11]
Gap Uncertainty has been studied for CPS, DNNs and robot foundation models — not yet for LLMs that generate or assess test artefacts.
Notes: Three lines of your work that this PhD builds on. First, uncertainty-wise testing of CPS, from the U-Taxonomy to uncertainty-aware oracles and, most recently, uncertainty and quality of VLA-enabled robots. Second, ADS scenario generation and robustness-guided falsification. Third, oracles and industrial CPS, especially the elevator case studies with Mondragon. To my knowledge none of these quantify the uncertainty of LLMs that generate the test artefacts themselves — that is the gap.

## Slide 5: Uncertainty of LLM outputs: what transfers to test artefacts
Idea | Evidence | What I take for test artefacts
Semantic entropy | Cluster sampled answers by meaning; entropy over clusters [23, 24] | Meaning of a test = what it does when executed → behavioural clusters
Self-consistency | Disagreement among sampled outputs flags hallucination [25] | Black-box: works with ChatGPT-class models without log-probs
UQ for LLMs in SE | Exploratory study of LLM uncertainty, incl. code tasks [26] | Measures ≠ correctness of executable, safety-relevant tests
UQ for DL supervision | Uncertainty monitors for fail-safe DL systems [28, 4] | Risk-based reject option → triage of generated tests
Key idea For an executable test, two samples mean the same thing if they make the system behave the same way. That gives a CPS-specific variant of semantic entropy: behavioural entropy.
Notes: From the ML literature I take two ideas: semantic entropy, which clusters sampled answers by meaning, and self-consistency, which needs only black-box access. The key adaptation: for an executable test the meaning is its behaviour on the system — so I cluster sampled tests by what they do in simulation. That is behavioural entropy.

## Slide 6: My starting point: an LLM test generator that trusts blindly
Requirements & specs
RAG over docs
LLM agents
Tests & scripts
Execution
Report
Trust today: hand-written rules
Schema validation and JSON repair of LLM output
Grounding checks: references and quotes must exist in the source
AI-only expectations are parked as NEEDS_REVIEW
Fault-injection gate: a test must fail on a corrupted system
The blind spot
Rules are binary and uncalibrated: pass the gate = trusted
A valid, grounded test can still miss the requirement or carry a wrong oracle
No signal says which tests a human must look at
No link between confidence and safety risk
Notes: This is the tool I built for daily testing work: requirement documents go through retrieval into LLM agents that produce test cases and scripts, which are executed and reported. Trust is handled by rules: schema checks, grounding checks, a review flag for AI-only expectations and a fault-injection gate. These catch malformed output, but they are binary: once a test passes the gate it is trusted. The tool cannot tell which of the well-formed tests are wrong — that is the blind spot this research targets.

## Slide 7: UQ-TestGen: an uncertainty-aware end-to-end pipeline
Requirement
natural language
N samples
LLM: scenario + oracle + confidence
Rule gate
schema & physics (v1)
Simulate
highway-env, ACC/AEB SUT
Quantify
4 uncertainty signals
Triage
accept / review / reject
Ground truth
8 seeded faults (research)
System under test: adaptive cruise control with emergency braking and lane keeping in highway-env [29]. Green = ego, blue = scripted traffic.
What is new vs. v1
Sample N tests instead of one
Uncertainty without ground truth
Risk-based triage replaces the binary gate
Fault-injection ground truth to evaluate the signals
Notes: I re-targeted the tool to an autonomous-driving function. For a requirement, the LLM is sampled N times; each sample is a driving scenario, an STL-style oracle and a self-reported confidence. The rule gate from v1 stays. Valid tests run in highway-env against an adaptive cruise control with emergency braking. Then four uncertainty signals are computed — no ground truth needed — and drive a triage decision. Only in research mode do we compute ground truth by running every test against eight seeded faults.

## Slide 8: Four uncertainty signals — no ground truth needed
Verbalised confidence
U = 1 − c
The LLM's own probability that the test is correct. Baseline.
Structural entropy
U = −log p(cluster) / log N
Cluster samples by oracle templates, event types and traffic layout — semantic entropy on the artefact [23].
Behavioural entropy (new)
U = −log p(behaviour) / log N
Cluster samples by what they do on the SUT: own verdict, collision, emergency braking, minimum-gap band.
Oracle disagreement
U = disagreeing peers / (N − 1)
Apply every peer's oracle to this sample's trace; disagreement means an ambiguous requirement.
Combined score = mean(structural, behavioural); oracle disagreement was uninformative on a development round and is reported only.
Notes: Four signals. Verbalised confidence is the baseline. Structural entropy clusters samples by what they look like. Behavioural entropy, my CPS-specific adaptation, clusters them by what they do when executed. Oracle disagreement cross-applies the oracles. I fixed the design on a development round and evaluated it on a fresh held-out round, to avoid tuning on the test data.

## Slide 9: Demo: one requirement, end to end, live LLM
What you see
R6: a cut-out reveals a stopped car
8 samples from gpt-5.6-luna
Live stages: generate → gate → simulate → quantify → triage → ground truth
Most uncertain test = the irrelevant one
Replay on a seeded fault: the oracle catches it
1 min 44 s · recorded from the running prototype
Notes: [Play video, about 1:44.] Requirement R6: the lead car changes lane and reveals a stopped car. Eight tests are sampled live. You can see each stage complete. The batch has low structural but some behavioural entropy. Five tests are auto-accepted, three go to review. The most uncertain test turns out to be the one that does not exercise the requirement. Finally the same test is replayed on a faulty variant and its oracle catches the fault.

## Slide 10: Experiment: 210 generated tests, 1,890 simulations
7
ACC requirements
time gap, braking, cut-in, set speed, stop & go, cut-out, comfort
3
LLMs via ChatGPT login
gpt-5.6-luna · gpt-5.6-terra · gpt-6-astra
10
samples per requirement
independent sessions, N = 10
8
seeded controller faults
gap, AEB, perception, actuator, logic
Ground truth per generated test
Correct: scenario exercises the requirement inside its ODD, and its oracle agrees with the reference formalisation on the correct SUT and all 8 faulty versions
Effective: mutation score of the test's own oracle
Method: metric design fixed on a development round (5 requirements); all numbers here from a fresh held-out round
Notes: Setup: seven requirements of an ACC, three ChatGPT-class models, ten samples each — 210 tests. Each test runs on the correct controller and eight seeded faults, so 1,890 simulations. A test is correct only if it exercises the requirement and its oracle agrees with my reference formalisation on all nine versions. I designed the metrics on a development round and report a fresh held-out round.

## Slide 11: Behavioural entropy beats the LLM's self-confidence
Chart: AUROC for detecting incorrect tests (0.5 = random)
| Verbalised conf. | Structural | Behavioural | Oracle disagr. | Combined
All tests (pooled) | 0.74 | 0.67 | 0.9 | 0.46 | 0.89
Within one requirement × model | 0.62 | 0.55 | 0.71 | 0.49 | 0.71
0.90
AUROC of behavioural entropy vs. 0.74 for the LLM's own confidence
Ranks the 17 incorrect tests (of 210) mostly at the top
Batch level: behavioural entropy vs. share of correct tests, Spearman ρ = -0.85
Honest caveat: within one requirement the signal drops to 0.71 — it mostly flags hard requirements
Held-out round, 210 tests; within-batch AUROC averaged over the 6 batches that contain incorrect tests.
Notes: On the held-out round, behavioural entropy detects incorrect tests with AUROC 0.90, against 0.74 for the model's own confidence. At batch level, the more behaviourally diverse the samples, the fewer of them are correct: rho -0.85. But I want to be honest: within a single requirement the signal is weaker, 0.71. Much of what it captures is that some requirements are hard. Per-test discrimination is my first research gap.

## Slide 12: Risk-based triage: 77% auto-accepted at 98.8% precision
Chart: Accept the least uncertain tests first
162
Auto-accept
160 correct · precision 99%
39
Human review
30 correct · precision 77%
9
Reject / regenerate
3 correct · precision 33%
Cost: ~16 s and ~2900 tokens per sample; ~1.0 s to simulate one test on 9 versions.
Accepting all tests gives 92% correct. Thresholds (accept ≤ 0.25 < review < 0.55 ≤ reject) are heuristic; calibrating them against risk is objective O2.
Notes: Turning uncertainty into decisions: accepting the least uncertain tests first keeps precision near 100% until about 70% coverage. With fixed thresholds, 162 of 210 tests are auto-accepted and 160 of them are correct; the review bucket is where the errors concentrate. These thresholds are heuristics, so calibrating them against safety risk is objective 2. I also log cost: N samples multiply the LLM cost, which is a non-functional trade-off for objective 3.

## Slide 13: What the demo cannot do yet becomes the research agenda
Gap seen in the demo | Research direction | Obj.
Per-test signal is weak within a requirement (AUROC 0.71); black-box only | White-box (log-prob) and trajectory-level metrics; semantic oracle equivalence; calibration | O1
Thresholds are heuristic; risk ignores the severity of the requirement | Risk = uncertainty × consequence; conformal / selective guarantees; cost-aware review budget | O2
Uncertainty vs. effectiveness only hinted (ρ = -0.28 with mutation score); cost of N samples | Large study: correctness, fault detection, flakiness, latency and token cost vs. uncertainty | O3
3 hosted LLMs, 1 simulator, 1 SUT, seeded faults | Open-source ACPS + industrial cases + InnoGuard platform; newer models; quantum ML models | O4
Notes: Each limitation of the demo maps onto one objective. The per-test signal is weak and black-box only — new metrics, O1. Thresholds are heuristic and ignore severity — risk methods, O2. The relation between uncertainty, effectiveness and cost is only hinted — a large empirical study, O3. And everything ran on three hosted models and one simulator — generalisation to industrial cases, the InnoGuard platform, newer models and quantum ML, O4.

## Slide 14: Research questions and how I will answer them
RQ1
Which uncertainty metrics best predict the correctness of AI-generated test artefacts?
Metric suite: behavioural / semantic / oracle / white-box; AUROC, calibration error; LLMs and VLMs as generators and judges
RQ2
How can uncertainty support risk-based acceptance of generated artefacts?
Risk model linking uncertainty to hazard severity; selective-prediction guarantees; review-effort savings in user studies
RQ3
How does uncertainty relate to effectiveness and non-functional properties?
Mutation score, failure severity, flakiness, execution time and token cost; mixed-effects statistics
RQ4
Do the metrics transfer to advanced and quantum ML models?
Re-apply metrics to newer foundation models and to QML-based oracles/predictors [20, 21]
Notes: Four research questions, one per objective, each with its method. Evaluation will use open-source ACPS such as highway-env or more realistic simulators, industrial case studies through the network — for example the elevator systems studied with Mondragon — and the InnoGuard demonstration platform, always with fault-injection or expert ground truth and proper statistics.

## Slide 15: 36-month plan with secondment and publications
Year 1
Year 2
Year 3
WP1 Survey & ACPS benchmark
WP2 UQ metrics (O1)
WP3 Uncertainty vs. quality study (O3)
WP4 Risk & trust methods (O2)
Secondment · Mondragon
WP5 Industrial & InnoGuard eval.
WP6 Advanced & quantum ML (O4)
Thesis
P1 mapping study
P2 metrics · ICST/ISSTA
P3 industrial study
P4 journal · TOSEM/TSE
P5 QML · ASE/ICSE
Publications
Notes: A 36-month plan. Year 1: a mapping study and an open ACPS benchmark, then the first metric suite. Year 2: the large empirical study on uncertainty versus quality and cost, risk methods, and the planned secondment at Mondragon to apply them to an industrial CPS. Year 3: evaluation on industrial cases and the InnoGuard platform, then the quantum ML extension with the adjacent project, and the thesis. Five planned papers; dates of the secondment are indicative and would follow the network's schedule.

## Slide 16: Expected contributions to InnoGuard
Metrics
Uncertainty metrics for AI-generated test artefacts, incl. behavioural entropy for executable CPS tests
Methods
Risk-based acceptance of AI-generated artefacts with calibrated, safety-aware thresholds
Evidence
Empirical laws linking uncertainty to correctness, fault detection and cost across models
Open science
Open benchmark, tool and replication packages; integration with the InnoGuard platform
Dissemination & network
Venues: ICSE, FSE, ASE, ISSTA, ICST; TOSEM, TSE, EMSE
Joint papers across the network, building on the team's foundation-model road maps [10, 11]
Secondment at Mondragon: industrial CPS case and oracle expertise
Training, summer schools and outreach of the doctoral network
Notes: Four contributions: metrics, risk methods, empirical evidence and open artefacts, published at the main SE venues and developed jointly across the network, with the Mondragon secondment as the industrial anchor.

## Slide 17: Why me, why this team
CPS tester by training automotive ECU testing, standards and test benches
Verification researcher falsification and test generation for controller software
Builder of AI testing tools a working uncertainty-aware prototype, today
Thank you
zavinhle@gmail.com
Notes: To close: I bring CPS testing practice, verification research and hands-on AI tooling, and the team brings the leading work on uncertainty-wise CPS testing, ADS testing and industrial oracles. I would be glad to turn this prototype into a PhD within InnoGuard. Thank you — I look forward to your questions.

## Slide 18: From automotive test benches to AI-driven testing
2019–23
B.S. Electrical & Electronics Eng.
HCMC Univ. of Technology, honors program · GPA 8.27/10
2022
Embedded SW intern
Drivers, firmware unit & functional testing
2022–24
Embedded SW test engineer · Bosch
Automotive ECU testing for OEMs · AUTOSAR, MISRA-C, ASPICE, CAPL
2024–26
M.S. Computer Science · KNU
Software Safety Eng. Lab · GPA 4.25/4.30 · falsification & property-based testing
2026–
Software test engineer · industry
Web/API/system testing · LLM, RAG & MCP-based test generation
Thesis Towards Efficient Function Abstraction via Active Learning for Property Falsification (advisor: Prof. Yunja Choi)
Papers Test generation for property checking (KCC 2025); stateful system, stateless techniques: test generation for controller software (KCSE 2026), with S. Hong and Y. Choi
Notes: My path goes from hardware to automotive software testing at Bosch, where I tested ECU software against AUTOSAR and MISRA rules, to research on falsification and test generation for controller software at Kyungpook National University, and now to building LLM-based test generation in industry. The common thread: making automated testing of safety-relevant software trustworthy.

## Slide 19: What I bring to the preferred profile
Testing cyber-physical systems
Functional and system testing of automotive ECUs (CAN, CAPL, ETAS INCA); robotics (ROS/ROS2) and embedded domains
Verification research
Falsification of safety and security properties, function abstraction via active learning, property-based testing — robustness-guided search like FalsifAI [14]
LLMs for quality engineering
LLM-assisted test-case generation, RAG over requirements, MCP-based agentic test workflows used in daily industrial testing
Python & empirical studies
Python, C/C++, TypeScript; controlled experiments on test generators (KCC'25, KCSE'26); the prototype and experiment in this talk
Notes: Mapping the advert's preferred profile to evidence: CPS testing from Bosch; verification research from my master's — my falsification work is close in spirit to Prof. Arcaini's robustness-guided falsification; LLMs for testing from my current work; and Python plus empirical research, which this talk also demonstrates.

## Slide 20: Backup · Results per model and requirement
Model | Valid | Correct | Mutation score | Self-confidence | Latency | Tokens
gpt-5.6-luna | 100% | 87% | 22% | 97% | 13.9 s | 2546
gpt-5.6-terra | 100% | 89% | 25% | 94% | 16.9 s | 2526
gpt-6-astra | 100% | 100% | 27% | 97% | 16.5 s | 3501
Chart: 
| R1 | R2 | R3 | R4 | R5 | R6 | R7
Share of correct tests | 1 | 1 | 0.8 | 1 | 0.93 | 0.77 | 0.93
Mean combined uncertainty | 0.02 | 0.04 | 0.33 | 0.13 | 0.07 | 0.19 | 0.15
Notes: Per model: the strongest model, gpt-6-astra, produced only correct tests, so uncertainty matters most for cheaper models. Per requirement: the cut-in (R3) and cut-out (R6) requirements are hardest, and they also have the highest uncertainty.

## Slide 21: Backup · Threats to validity and mitigations
Threat | In this prototype | Mitigation in the PhD
Construct | Correctness = agreement with my reference formalisation; mutants approximate real faults | Expert-validated oracles; real fault data from industrial partners
Internal | Metric design chosen on a development round; heuristic thresholds | Held-out evaluation; pre-registered designs; calibration on separate data
External | One SUT, one simulator, 7 requirements, 3 hosted LLMs | Open-source ACPS, industrial cases, InnoGuard platform, open-weight models
Conclusion | 17 incorrect tests in 6 batches; small N per batch | Larger N, repeated runs, effect sizes and confidence intervals
Notes: Main threats: my reference formalisation and synthetic mutants define ground truth; the design was chosen on a development round; and the scale is small. Each has a concrete mitigation in the PhD plan.

## Slide 22: Backup · Towards uncertainty of quantum ML models (O4)
Starting point: QML is already used for test oracles of autonomous mobile robots and QoS prediction of elevator software [20, 21]
Sources of uncertainty: shot noise, hardware noise and model (epistemic) uncertainty add to data uncertainty
Transfer test: do behavioural / sampling-based metrics still predict wrong oracle verdicts when the model is quantum? Repeated shots are natural samples
Coverage & mutation for quantum programs as ground-truth tools [19]
Road map: quantum AI for software engineering [22]
Notes: For objective 4, the adjacent project on quantum ML: shot-based sampling gives a natural analogue to sampling an LLM, so the same disagreement-based metrics can be tested, with quantum noise as an extra uncertainty source.

## Slide 23: References (1/2)
[1] M. Zhang, S. Ali, and T. Yue, "Uncertainty-wise test case generation and minimization for cyber-physical systems," J. Syst. Softw., vol. 153, pp. 1–21, 2019, doi: 10.1016/j.jss.2019.03.011.
[2] M. Zhang, S. Ali, T. Yue, R. Norgren, and O. Okariz, "Uncertainty-wise cyber-physical system test modeling," Softw. Syst. Model., vol. 18, no. 2, pp. 1379–1418, 2019, doi: 10.1007/s10270-017-0609-6.
[3] M. Zhang, B. Selic, S. Ali, T. Yue, O. Okariz, and R. Norgren, "Understanding uncertainty in cyber-physical systems: A conceptual model," in Proc. ECMFA, LNCS 9764, 2016, pp. 247–264, doi: 10.1007/978-3-319-42061-5_16.
[4] F. O. Catak, T. Yue, and S. Ali, "Uncertainty-aware prediction validator in deep learning models for cyber-physical system data," ACM TOSEM, vol. 31, no. 4, pp. 1–31, 2022, doi: 10.1145/3527451.
[5] L. Han, S. Ali, T. Yue, A. Arrieta, and M. Arratibel, "Uncertainty-aware robustness assessment of industrial elevator systems," ACM TOSEM, vol. 32, no. 4, pp. 1–51, 2023, doi: 10.1145/3576041.
[6] P. Valle, A. Arrieta, L. Han, S. Ali, and T. Yue, "Defining and generating multi-level and uncertainty-wise test oracles for cyber-physical systems," Softw. Syst. Model., vol. 24, no. 3, pp. 679–704, 2025, doi: 10.1007/s10270-025-01271-8.
[7] P. Valle, C. Lu, S. Ali, and A. Arrieta, "Evaluating uncertainty and quality of vision-language-action-enabled robots," arXiv:2507.17049, 2025.
[8] J. Wu, C. Lu, A. Arrieta, T. Yue, and S. Ali, "Reality bites: Assessing the realism of driving scenarios with large language models," in Proc. IEEE/ACM FORGE, 2024, pp. 40–51, doi: 10.1145/3650105.3652296.
[9] H. Sartaj, J. Boudjadar, M. Frasheri, S. Ali, and P. G. Larsen, "Identifying uncertainty in self-adaptive robotics with large language models," IEEE Softw., vol. 43, no. 1, pp. 89–97, 2026, doi: 10.1109/MS.2025.3620578.
[10] C. Lu, P. Valle, J. Wu, E. Isaku, H. Sartaj, A. Arrieta, and S. Ali, "Foundation models for software engineering of cyber-physical systems: The road ahead," ACM TOSEM, vol. 35, no. 9, pp. 1–58, 2026, doi: 10.1145/3830403.
[11] S. Ali, P. Arcaini, and A. Arrieta, "Foundation models for the digital twins creation of cyber-physical systems," in Proc. ISoLA 2024, LNCS, Springer, 2025, pp. 9–26, doi: 10.1007/978-3-031-75390-9_2.
[12] A. Calò, P. Arcaini, S. Ali, F. Hauer, and F. Ishikawa, "Generating avoidable collision scenarios for testing autonomous driving systems," in Proc. IEEE ICST, 2020, pp. 375–386, doi: 10.1109/ICST46399.2020.00045.
[13] T. Laurent, S. Klikovits, P. Arcaini, F. Ishikawa, and A. Ventresque, "Parameter coverage for testing of autonomous driving systems under uncertainty," ACM TOSEM, vol. 32, no. 3, pp. 1–31, 2023, doi: 10.1145/3550270.
[14] Z. Zhang, D. Lyu, P. Arcaini, L. Ma, I. Hasuo, and J. Zhao, "FalsifAI: Falsification of AI-enabled hybrid control systems guided by time-aware coverage criteria," IEEE TSE, vol. 49, no. 4, pp. 1842–1859, 2023, doi: 10.1109/TSE.2022.3194640.
[15] Z. Zhang, D. Lyu, P. Arcaini, L. Ma, I. Hasuo, and J. Zhao, "Effective hybrid system falsification using Monte Carlo tree search guided by QB-robustness," in Proc. CAV, LNCS, 2021, pp. 595–618, doi: 10.1007/978-3-030-81685-8_29.
[16] A. Arrieta, J. Ayerdi, M. Illarramendi, A. Agirre, G. Sagardui, and M. Arratibel, "Using machine learning to build test oracles: An industrial case study on elevators dispatching algorithms," in Proc. IEEE/ACM AST, 2021, pp. 30–39, doi: 10.1109/AST52587.2021.00012.

## Slide 24: References (2/2)
[17] J. Ayerdi, V. Terragni, A. Arrieta, P. Tonella, G. Sagardui, and M. Arratibel, "Generating metamorphic relations for cyber-physical systems with genetic programming: An industrial case study," in Proc. ESEC/FSE, 2021, pp. 1264–1274, doi: 10.1145/3468264.3473920.
[18] A. Arrieta, P. Valle, J. A. Agirre, and G. Sagardui, "Some seeds are strong: Seeding strategies for search-based test case selection," ACM TOSEM, vol. 32, no. 1, pp. 1–47, 2023, doi: 10.1145/3532182.
[19] S. Ali, P. Arcaini, X. Wang, and T. Yue, "Assessing the effectiveness of input and output coverage criteria for testing quantum programs," in Proc. IEEE ICST, 2021, pp. 13–23, doi: 10.1109/ICST49551.2021.00014.
[20] X. Wang, Q. Xu, P. Arcaini, S. Ali, and T. Peyrucain, "Quantum machine learning-based test oracle for autonomous mobile robots," in Proc. IEEE/ACM ASE, 2025, pp. 3695–3706, doi: 10.1109/ASE63991.2025.00306.
[21] X. Wang, S. Ali, A. Arrieta, P. Arcaini, and M. Arratibel, "Application of quantum extreme learning machines for QoS prediction of elevators' software in an industrial context," in Companion Proc. ACM FSE, 2024, pp. 399–410, doi: 10.1145/3663529.3663859.
[22] X. Wang, S. Ali, and P. Arcaini, "Quantum artificial intelligence for software engineering: The road ahead," ACM TOSEM, vol. 35, no. 9, pp. 1–42, 2026, doi: 10.1145/3827610.
[23] L. Kuhn, Y. Gal, and S. Farquhar, "Semantic uncertainty: Linguistic invariances for uncertainty estimation in natural language generation," in Proc. ICLR, 2023. arXiv:2302.09664.
[24] S. Farquhar, J. Kossen, L. Kuhn, and Y. Gal, "Detecting hallucinations in large language models using semantic entropy," Nature, vol. 630, no. 8017, pp. 625–630, 2024, doi: 10.1038/s41586-024-07421-0.
[25] P. Manakul, A. Liusie, and M. J. F. Gales, "SelfCheckGPT: Zero-resource black-box hallucination detection for generative large language models," in Proc. EMNLP, 2023, pp. 9004–9017, doi: 10.18653/v1/2023.emnlp-main.557.
[26] Y. Huang, J. Song, Z. Wang, S. Zhao, H. Chen, F. Juefei-Xu, and L. Ma, "Look before you leap: An exploratory study of uncertainty analysis for large language models," IEEE TSE, vol. 51, no. 2, pp. 413–429, 2025, doi: 10.1109/TSE.2024.3519464.
[27] J. Wang, Y. Huang, C. Chen, Z. Liu, S. Wang, and Q. Wang, "Software testing with large language models: Survey, landscape, and vision," IEEE TSE, vol. 50, no. 4, pp. 911–936, 2024, doi: 10.1109/TSE.2024.3368208.
[28] M. Weiss and P. Tonella, "Fail-safe execution of deep learning based systems through uncertainty monitoring," in Proc. IEEE ICST, 2021, pp. 24–35, doi: 10.1109/ICST49551.2021.00015.
[29] E. Leurent, "An environment for autonomous driving decision-making," GitHub repository, 2018. https://github.com/Farama-Foundation/HighwayEnv
[30] InnoGuard: Hybrid and Generative Intelligence for Trustworthy Autonomous Cyber-Physical Systems, Horizon Europe MSCA Doctoral Network, GA No. 101169233, 2024–2028. https://cordis.europa.eu/project/id/101169233
[31] Z. V. Le, S. Hong, and Y. Choi, "Performance of test generation techniques on property checking: A case study," Korea Congress of Computing (KCC), 2025.
[32] Z. V. Le, S. Hong, and Y. Choi, "Stateful system, stateless techniques: Initial assessment on test generation for property checking of controller software," Korea Conference on Software Engineering (KCSE), 2026.